## Slide 1: A Material Classification Protocol for a Mechatronic Platform
Giovanni Luca Biundo
Ivan Brillo
A.Y 2024/2025
Data Mining and Machine Learning Project

## Slide 2
INTRODUCTION TO THE PROBLEM
Accurate material classification is critical in engineering and biomedical fields.
Traditional methods (e.g., visual inspection, destructive testing) are often impractical.
GOAL: Develop a non-destructive, automated classification method using machine learning.
Challenges:
Extracting relevant features from heterogeneous sensor data
Handling boundary effects and experimental variability
Custom mechatronic platform developed for precise material testing.
Tri-axial motorized stage.
Linear actuator for controlled interaction
High-precision load cell for sensitive force measurement
MACHINE USED

## Slide 3
MACHINE USED
Challenges:
Extracting relevant features from heterogeneous sensor data
Handling boundary effects and experimental variability
Accurate material classification is critical in engineering and biomedical fields.
Traditional methods (e.g., visual inspection, destructive testing) are often impractical.
GOAL: Develop a non-destructive, automated classification method using machine learning.
Custom mechatronic platform developed for precise material testing.
Tri-axial motorized stage.
Linear actuator for controlled interaction
High-precision load cell for sensitive force measurement
DamasconeA :
2 measurments
TRAIN-SET
DamasconeB :
1 measurment
TEST-SET

## Slide 4
MACHINE USED
Custom mechatronic platform developed for precise material testing.
Tri-axial motorized stage.
Linear actuator for controlled interaction
High-precision load cell for sensitive force measurement
DATASET : SAMPLES
DamasconeA :
2 measurments
DamasconeB :
1 measurment
TRAIN-SET
TEST-SET
81 x 81 grid of points
DATASET : TABLES

## Slide 5
DamasconeA :
2 measurments
DamasconeB :
1 measurment
DATASET : TABLES
81 x 81 grid of points
TRAIN-SET
TEST-SET
DATASET : SAMPLES

## Slide 6
DATASET : TABLES
81 x 81 grid of points
FEATURE EXTRACTION:
Signals Pre-processing
Extracted features: Stiffness, Tau, Entropy, Upstroke, Downstroke, Psteadystate, ForceOvershoot, ForceRelaxation, ForceRMS, DampingCoefficient, ContactArea, ForcePeakToPeak, Activity, Mobility, TkeoMean, CorrelationForcePosition, PeakRatio, SampleEntropy, LoadingSkewness, LoadingKurtosis, QuarticCoefficient.
RAW SIGNAL
GAUSSIAN SMOOTHING
NORMALIZATION
INTERPOLATION (1kHz)
CUBIC SPLINE
FEATURE EXTRACTION:
Feature Computation
STIFFNESS
UPSTROKE
DOWNSTROKE
DAMPING COEFFICIENT
MOBILITY
TKEO-MEAN

## Slide 7
FEATURE EXTRACTION:
Feature Computation
FEATURE EXTRACTION:
Signals Pre-processing
STIFFNESS
UPSTROKE
DOWNSTROKE
DAMPING COEFFICIENT
MOBILITY
TKEO-MEAN

## Slide 8
DATASET PREPROCESSING
SPATIAL SMOOTHING - MEDIAN
Perform a 3x3 spatial filtering using the median operation
Remove measurements noise and make the spatial data more homogenous
NaN HANDLING
We used NearestNDInterpolator to fill feature points gaps in our 2D grid

## Slide 9
DATASET PREPROCESSING
DATASET IMBALANCE - ADASYN
Works similar to SMOTE to perform minority classes oversample
But it favors points in low class density regions to start the oversampling and to generate points that are near the class decision boundaries
DB SPLITTING
We divided the three objects in train, validation and test datasets

## Slide 10
DATASET PREPROCESSING
SPATIAL SMOOTHING - MAXIMUM
SCALING
Avoid biases, improve Gradient Descent and regularization
Flatten features drift that arise from different experiment conditions
After detecting hard-spots points, we performed a 3x3 max filtering

## Slide 11
FEATURE SELECTION
GLOBAL WASSERSTEIN DISTANCE
MUTUAL INFORMATION
We want to find invariant features among experiments
Given two PDFs, one for training points and the other for validation points projected onto a single feature, their distance is defined as the minimum cost to transform one into the other

## Slide 12
FEATURE SELECTION
FEATURE SELECTION PIPELINE
PER-CLASS WASSERSTEIN DISTANCE
th1 ∈ [0.025, 0.15], th2 ∈ [0.025, 0.2] for the two distances (MI not considered)
For all the pairs of (th1, th2) find all the features sets with lower distances
For each feature set with same number of features, calculate the silhouette score and keep only the higher one (since features clusters are approximately convex)

## Slide 13
MODEL SELECTION AND HYPER-PARAMETERS TUNING
RandomizedSearchCV
ENSEMBLE MODEL AND CROSS VALIDATION
We define a randomized search over the features sets, the binary and multiclass models, and their hyperparameters
The best parameters set is chosen by f1-score macro
We defined a custom ensemble model with binary and multiclass classifiers
We perform a 2-fold cross validation, training before on train dataset and evaluating on validation and vice-versa

## Slide 14
PREDICT_PROBA METHOD
RandomizedSearchCV
ENSEMBLE MODEL
We define a randomized search over the features sets, the binary and multiclass models, and their hyperparameters
The best parameters set is chosen by f1-score macro
STANDARD CLASSIFIERS METHOD CAN’T BE USED DIRECTLY
CUSTOM METHOD :
Use STAGE 1 predict_proba :
For samples where the STAGE 1
assigned class 0 :
For samples where the STAGE 1
assigned class != 0 :
UNIFORM DISTRIBUTION
NUMBER OF CLASSES

## Slide 15
PREDICT_PROBA METHOD
For samples where the STAGE 1
assigned class != 0 :
Use STAGE 2 predict_proba :
From the definition of conditional probability :
We also have that :
Implication
Finally we have :

## Slide 16
RESULTS
BEST COMBINATIONS :
Best achieved f1-macro score during RandomSearchCV : 0.787

## Slide 17
RESULTS
CONFUSION MATRICES :
Test set: DamasconeB
Overall accuracy: 0.8383
Macro F1-score: 0.6438
SINGLE-VALUE METRICS :

## Slide 18
RESULTS
SINGLE-VALUE METRICS :
CONFUSION MATRICES :
PREDICTION MAP :

## Slide 19
PREDICTION MAP :
The classifier is still able to predict the right class for hard areas !
VALUABLE
FROM AN APPLICATION STANDPOINT
SINGLE-VALUE METRICS :

## Slide 20
MODEL EXPLAINATION: SHAP
SHAP PLOTS
SHAP values are defined over the predict_proba function of the model, thus they are on probability scale
SHAP value ϕijk = 0 indicates that feature j has no additional impact beyond the baseline expectation on class k
damping coefficient is the most important feature across all classes except class 1, where stiffness is more informative
Higher values of damping coefficient tend to decrease the probability of predicting class 3
Features that have SHAP values clustered near zero for a particular class are not informative or meaningful for that class
Class 3 SHAP values plot

## Slide 21
Massari, L.; Bulletti, A.; Prasanna, S.; Mazzoni, M.; Frosini, F.; Vicari, E.; Pantano, M.; Staderini, F.; Ciuti, G.; Cianchi, F.; et al. A Mechatronic Platform for Computer Aided Detection of Nodules in Anatomopathological Analyses via Stiffness and Ultrasound Measurements. Sensors 2019, 19, 2512, doi: https://doi.org/10.3390/s19112512
REFERENCES
Haibo He, Yang Bai, E. A. Garcia and Shutao Li, ”ADASYN: Adaptive synthetic sampling approach for imbalanced learning,” 2008 IEEE International Joint Conference on Neural Networks (IEEE World Congress on Computational Intelligence), Hong Kong, 2008, pp. 1322-1328, doi:10.1109/IJCNN.2008.4633969.

## Slide 22
THANK YOU FOR YOUR ATTENTION